## Slide 1
ENGINEERING DESIGN REVIEW
12 GHz RF jumpers
How to change the path from direct-through to a test connector
Architecture options, RF tradeoffs, layout rules, and a verification plan
RF part
DIRECT
NEXT
TEST
Prepared for technical discussion

## Slide 2
01 | PROBLEM DEFINITION
The design question is a controlled RF state change
KEY QUESTION
One node must support two mutually exclusive destinations without turning the unused branch into an RF problem.
RF component
PATH SELECT
SW / LINK / RELAY
NEXT RF
COMPONENT
TEST
CONNECTOR
State A
Direct path
State B
Test access
Is the test port a replacement path or a monitor port?
Must switching occur powered, unpowered, or only during service?
What are the allowed loss, isolation, VSWR, and lifetime?

## Slide 3
02 | RF REALITY
At 12 GHz, the interconnect is part of the circuit
DESIGN TARGETS
25 mm
free-space wavelength
~15-18 mm
typical guided wavelength
1 mm
is already a meaningful discontinuity
-20 dB
a useful first isolation target
What creates risk
A jumper or test feature adds length, pads, vias, connector launch geometry, and an unused branch. Each can create reflection and loss.
What must be measured
S-parameters across the full operating band
Insertion loss in both selected states
Return loss at component, switch, and test ports
Isolation from the selected path to the unused path
Do not choose the topology from DC continuity alone. Choose it from the RF error budget and the operating procedure.

## Slide 4
03 | REQUIREMENT SPLIT
There are two fundamentally different requirements
DECISION TREE
What does "test connector" need to do?
Replace the next component
for a measurement
Observe the signal
while the next component stays connected
Use a 1:2 selector
Use a coupler or splitter
Direct path is open when TEST is selected
Isolation protects the inactive destination
Best when test means "break in here"
Main path remains active
Test port receives a coupled, lower-power sample
Best for non-invasive monitoring or calibration

## Slide 5
04 | PASSIVE LINKS
Option 1: fixed PCB links are cheap, but not operationally flexible
LOW COST
RF IN
0 ohm /
solder link
NEXT
TEST
Assembly variant
Solder bridge or 0 ohm resistor selects one route
Coax pigtail or edge connector can expose the test node
No live switching; service requires rework or a build variant
Unused branch must be terminated, removed, or kept very short
Use when: low unit volume, factory configuration, and rework is acceptable. Avoid when technicians must switch repeatedly.

## Slide 6
05 | COAXIAL JUMPER
Option 2: a mechanical RF jumper gives service access without active electronics
SERVICEABLE
RF IN
JACK /
SOCKET
NEXT
Jumper installed
TEST
Options: 2-port coax jumper, removable shunt, or board-to-board RF cable
Excellent passive linearity and power handling when well matched
Connector launch and repeated mating dominate performance
Need keyed access, ESD handling, strain relief, and a defined torque/process
Best fit: occasional field or lab switching where the RF path must be physically obvious.

## Slide 7
06 | ACTIVE SELECTION
Option 3: an RF switch is the cleanest repeatable 1:2 selector
RECOMMENDED DEFAULT
RF IN
SPDT RF
SWITCH
CTRL
NEXT
TEST
Series SPDT: low bill of materials, finite isolation, control sequencing required
Reflective vs absorptive: decide how the unused throw is terminated
Choose switch family for 12 GHz, not just “microwave capable”
Check insertion loss, isolation, P1dB / IP3, ESD, control voltage, and switching lifetime
Default architecture for a production product: place the switch at the branch point and keep both routes 50 ohm.

## Slide 8
07 | OTHER ARCHITECTURES
Option 4: relays, MEMS, and external instruments trade speed for RF quality
WHEN TO USE
Architecture
RF strength
Main penalty
Good fit
Electromechanical relay
Very good isolation / linearity
Slow; wear; coil drive; size
Power-off state, high isolation, low switching count
RF MEMS switch
Low loss; high linearity; low power
Specialized; control/packaging; slower than IC
High-performance instrumentation or niche products
Coaxial RF switch box
Excellent connectorized RF; easy debug
Cost, volume, external wiring
Lab fixture, characterization, prototype
Probe / pogo / VNA fixture
No permanent connector on product
Repeatability, contact force, calibration
Manufacturing test, not normal operation
A relay can be the right answer when the RF budget is tight and switching is infrequent. An IC switch is usually the better product compromise.

## Slide 9
08 | NON-INVASIVE TEST ACCESS
If the test connector must monitor, do not switch the main path
ALTERNATIVE
RF IN
DIRECTIONAL
COUPLER
NEXT
TEST
Coupled sample
Main signal remains connected to NEXT in every state
Coupling factor sets test-port power and measurement dynamic range
Add a switch or attenuator at TEST if multiple instruments share the port
Terminate unused test paths with a good 50 ohm load
Use this when "test" means observe, not replace. It avoids interrupting the system path, but adds permanent insertion loss and a coupler footprint.

## Slide 10
09 | LAYOUT RULES
The RF layout determines whether the chosen topology survives 12 GHz
PCB IMPLEMENTATION
1
Launch cleanly
Controlled-impedance geometry; short pad transitions; connector footprint from the vendor.
2
Keep the branch compact
Place switch / link at the decision node. Minimize the open stub to the inactive route.
3
Protect the return path
Continuous reference plane; via fence around the RF line; avoid unnecessary layer changes.
4
Plan for calibration
Put test connector and calibration reference plane where the VNA can actually de-embed to.
5
Control mechanics
Connector torque, mating cycles, ESD, cable bend radius, and access direction are RF requirements.
At 12 GHz, “short” is an RF statement: compare physical length to guided wavelength and simulate or measure the launch.

## Slide 11
10 | TRADEOFF MATRIX
Select the topology by the dominant constraint, not by habit
DECISION GUIDE
Need
Preferred architecture
Why
Watch-outs
Factory variant
Solder link / 0 ohm
Lowest cost and loss if route is fixed
Rework and unused branch
Occasional service
Mechanical coax jumper
Visible, passive, easy to understand
Mating and connector launch
Repeatable product switching
SPDT RF switch
Fast, controlled, compact
Loss, isolation, control state
Maximum isolation
EM relay / coax switch
Strong off-state behavior
Size, speed, wear, cost
Continuous monitoring
Directional coupler
No interruption of main path
Permanent loss and sample level
Manufacturing test
Pogo / probe fixture
No product connector required
Contact repeatability and calibration

## Slide 12
11 | RECOMMENDATION
A practical baseline is an SPDT switch plus a connectorized test route
BASELINE DESIGN
RF
COMPONENT
SPDT
12 GHz+
NEXT RF
COMPONENT
TEST
CONNECTOR
Default state: DIRECT
Test state: TEST
Use a switch specified beyond 12 GHz with characterized S-parameters
Keep both switch throws 50 ohm and route the test throw to a robust connector
Define break-before-make or make-before-break behavior
Add interlock / state indication so the tester knows which path is active
If the requirement is observation rather than substitution, replace the SPDT with a directional coupler and keep NEXT permanently connected.

## Slide 13
12 | VERIFICATION PLAN
Verification must prove both RF performance and real-world usability
EXIT CRITERIA
01
Simulate
EM model of switch / link, pads, vias, connector launch, and inactive branch.
02
Calibrate
VNA calibration at the intended reference plane; document adapters and de-embedding.
03
Measure
S11 / S22, insertion loss, isolation, phase, and power handling across the full band.
04
Stress
Mating cycles, torque, cable movement, temperature, vibration, ESD, and state transitions.
05
Release
Freeze footprint, control truth table, connector process, acceptance limits, and test record.
Minimum decision package
Operating band | max loss | return loss | isolation | power | switching mode | mating life | environmental profile
Recommendation: start with the SPDT baseline, then downgrade to a passive link only if the use case is truly configuration-only.

## Slide 14
13 | CLOSING
Takeaway: define "test" first, then choose the jumper
NEXT STEP
Replacement path
SPDT / relay / mechanical jumper
Monitor path
Directional coupler / splitter
Factory-only variant
Solder link / 0 ohm / PCB option
Manufacturing access
Probe or pogo fixture
The robust 12 GHz design is the one that makes the inactive path electrically quiet, mechanically repeatable, and measurable.
Open design inputs: frequency span, power, connector family, switching frequency, environment, and whether "test" replaces or monitors the next component.

## Slide 15
14 | THESIS-FOCUSED CONCEPT
For a bachelor thesis, treat the 1:2 selector as an assembly option
LOW-COST PATH
The selector is not changed while powered. You change which RF link is populated, then measure the new configuration.
RF
COMPONENT
SELECTOR
NODE
J_DIRECT
0 ohm link
J_TEST
0 ohm link
NEXT
TEST
CONNECTOR
Populate exactly one link at a time:
J_DIRECT OR J_TEST, never both.
This is a reconfigurable prototype, not a live RF switch.

## Slide 16
15 | POPULATION PLAN
Use three build states: direct, test, and safe open
BOM + ASSEMBLY
Build state
J_DIRECT
J_TEST
Connector
Purpose
A: Direct / final
POPULATED
DNP
DNP or 50 ohm
Normal signal path to the next component.
B: Test / measure
DNP
POPULATED
POPULATED
Route the component output to the VNA or test instrument.
C: Safe open
DNP
DNP
DNP
Debug / isolation state; no complete path.
DNP = do not populate; it is an assembly instruction, not an electrical component.
Keep one spare PCB or a small rework area because repeated soldering can damage pads.
Record the exact population state on every measurement file and PCB photograph.

## Slide 17
16 | RF TOPOLOGY DETAILS
The low-cost selector works only if the inactive branch is controlled
DO NOT LEAVE A STUB
Good: branch point is compact
NODE
NEXT
TEST
Keep the distance from NODE to either link as short as possible.
Bad: long open branch
NODE
NEXT
OPEN /
CONNECTOR
An unselected 50 ohm branch is not automatically harmless. Terminate it, remove it, or make the stub electrically very short.

## Slide 18
17 | FINAL-STATE STRATEGY
Use a connector only during characterization, then depopulate or terminate it
PRACTICAL BUILD
1
Characterization PCB
J_DIRECT DNP
J_TEST POPULATED
Test connector fitted
2
Measure components
VNA -> TEST
Measure each block
Save S-parameters
3
Commit final path
J_DIRECT POPULATED
J_TEST DNP
Connector DNP or 50 ohm
Do not treat the test connector as “free” once it is left open: the connector launch and branch still load the circuit.
If the connector remains fitted in the final board, connect a suitable 50 ohm termination when the port is unused.
If budget allows only one board spin, put the test connector on a small detachable coupon or a breakaway edge section.

## Slide 19
18 | MEASUREMENT WORKFLOW
Measure one block at a time, but always define the reference plane
VNA METHOD
01
Calibrate
SOLT or TRL at the connector / fixture reference plane
02
Connect
Use short, known-good 50 ohm cables and torque connectors consistently
03
Measure
S11, S21, and phase across the complete frequency span
04
Compare
Check against the same fixture and cable baseline
05
Record
File name includes PCB ID, build state, component ID, and date
The measurement is only useful if the fixture contribution is known. First measure a through / thru standard or a known-good reference path.

## Slide 20
19 | TEST MATRIX
A simple test matrix makes the thesis results traceable
DATA RECORD
Item
Build state
What to measure
Expected question
UUT-1
B: TEST
S11 / S21
Does the component meet its datasheet behavior at 12 GHz?
J_TEST path
B: TEST
S11 / S21 / phase
How much does the test link and connector add?
J_DIRECT path
A: DIRECT
S11 / S21
Does the final route preserve the direct path?
Inactive branch
A: DIRECT
S11 / S21 at NEXT
Does the unused test branch disturb the direct route?
Repeatability
A and B x 3
S21 spread
Does rework or cable movement change the result?
Use the same frequency grid, IF bandwidth, power level, calibration, and cable routing for comparable results.

## Slide 21
20 | COMPONENT AND FOOTPRINT
Choose the 0 ohm implementation as an RF part, not a generic resistor
PART SELECTION
Package
Prefer a small package with a short current path; 0402 is easier to assemble, 0201 can reduce parasitic size.
Footprint
Use a symmetric 50 ohm launch into the link; avoid long rectangular pads that widen the line.
Solder bridge
Lowest BOM cost, but manual solder volume and repeatability are harder to control.
Rework
Add access, courtyard, and nearby ground; plan for wick / hot-air rework without lifting pads.
Important: a 0 ohm resistor is not an ideal RF short. Verify the chosen part and footprint with S-parameter data or measure the assembled link.

## Slide 22
21 | COMMON FAILURE MODES
Do not populate both links: that creates a splitter, not a selector
CHECK BEFORE POWER
NODE
NEXT
TEST
Both POPULATED
The RF component now sees two destinations in parallel.
Power splits and the two loads interact through the branch.
A test connector cable can change the final path response.
Document a visual inspection or continuity check before every VNA run.
Assembly rule: exactly one of J_DIRECT and J_TEST is populated for a valid 1:2 build state.

## Slide 23
22 | RECOMMENDED IMPLEMENTATION
Thesis-ready recommendation: one low-cost board, two controlled builds
FINAL PROPOSAL
Board design
50 ohm RF traces
Compact branch node
J_DIRECT and J_TEST footprints
Test connector footprint with DNP option
Clear silkscreen: DIRECT / TEST
Characterize
Populate J_TEST
Measure each component
Measure test route
Save raw Touchstone data
Compare against datasheet
Finalize
Populate J_DIRECT
DNP J_TEST
DNP or terminate connector
Repeat final measurement
Report difference
Evidence
Photos of both states
BOM population table
VNA calibration record
S11 / S21 plots
Uncertainty and limitations
This gives you a defensible thesis story: measure the device, quantify the test path, then quantify the impact of the final direct path.

## Slide 24
23 | AWR + KICAD WORKFLOW
Design the selector in four models, from simple to realistic
MODEL HIERARCHY
1
Ideal circuit
Check the logic: one input, two mutually exclusive outputs.
2
Transmission-line model
Check 50 ohm lines, branch length, pads, and connector launches.
3
EM model
Capture coupling, discontinuities, vias, and the real ground plane.
4
Measured board
Compare S-parameters and update the model assumptions.
Do not start in KiCad by drawing a beautiful board. Start by proving the RF topology and dimensions in AWR, then transfer the controlled geometry deliberately.

## Slide 25
24 | AWR PREPARATION
Step 1: freeze the design inputs before opening the simulator
INPUTS
01
Frequency
Start / stop frequency, for example 10 to 14 GHz if 12 GHz is the center.
02
Impedance
50 ohm system; define acceptable S11, S21, and isolation limits.
03
Stack-up
Substrate Dk, loss tangent, thickness, copper thickness, soldermask assumption.
04
Components
RF component package, pad dimensions, 0 ohm link package, connector footprint.
05
States
State A: J_DIRECT populated. State B: J_TEST populated. Never model both as the valid state.
06
Boundary
Define the VNA reference plane: board connector, component pin, or de-embedded plane.
Ask the PCB manufacturer for the controlled-impedance stack-up before selecting trace widths. Do not use a generic calculator value as the final dimension.

## Slide 26
25 | AWR SCHEMATIC
Step 2: build the ideal 1:2 selector schematic in AWR
FIRST SIMULATION
PORT 1
RF IN
RF
DEVICE
NODE
J_DIRECT
J_TEST
PORT 2
NEXT
PORT 3
TEST
Use ideal ports and an ideal switch/link first to verify the signal-flow logic.
Simulate State A and State B as separate schematics or separate link values.
Plot S21 for the selected route and S31 for the alternate route; confirm the inactive route is not accidentally connected.

## Slide 27
26 | TRANSMISSION-LINE MODEL
Step 3: replace ideal wires with AWR microstrip models
MSUB + MLIN
MSUB
Define substrate and copper stack-up
MLIN
Set width, length, metal thickness, and substrate
MTEE
Model the branch junction
MSTEP / MOPEN
Model width transitions and open ends where applicable
PORT
Set reference impedance and calibration reference
Parameterize before optimizing: line width W, branch length Lbranch, pad length Lpad, pad width Wpad, and connector transition dimensions.

## Slide 28
27 | MODELS AND DATA
Step 4: add realistic component and connector data
S-PARAMETERS
RF component
Use vendor S2P file if available. Check port order, impedance, frequency span, and de-embedding plane.
0 ohm link
Start with an ideal short, then replace it with vendor S-parameters or a measured coupon.
RF connector
Use a vendor model, launch model, or a measured connectorized reference.
Cables / adapters
Do not hide them in the DUT model. Calibrate or include their S-parameters explicitly.
Touchstone files normally use a .s1p, .s2p, or similar extension.
Confirm whether the file is measured at 50 ohm and whether it uses dB/angle or real/imaginary format.
Keep a copy of every model used in the thesis project folder and record its source.

## Slide 29
28 | AWR ANALYSIS
Step 5: simulate both valid population states and sweep the sensitive dimensions
OPTIMIZE
Case
Link definition
Plots
Decision
State A
J_DIRECT = short; J_TEST = open / terminated
S11 at input; S21 to NEXT; effect of inactive branch
State B
J_DIRECT = open; J_TEST = short
S11 at input; S21 to TEST; test-route loss
Sensitivity
Sweep W, Lbranch, Lpad, and connector launch
Find which dimension moves the 12 GHz response most
Acceptance
Add limits to the graphs
Pass / fail by frequency, not only at one marker
Use optimization only after the model is physically sensible. An optimizer can find a mathematically good but unmanufacturable geometry.

## Slide 30
29 | AWR EM
Step 6: use EM simulation for the branch, pads, and return path
AXIEM-STYLE EM
01
Create EM structure
Select the selector region, stack-up, ports, and ground boundary.
02
Draw physical metal
Include trace widths, branch, pads, vias, connector launch, and nearby copper.
03
Set ports
Place ports where the circuit model will connect; keep the reference plane intentional.
04
Sweep frequency
Use the same frequency range as the schematic simulation.
05
Export S-parameters
Use the EM result as a block in the circuit schematic.
EM is where the model begins to see the real branch discontinuity. Start with a small region around the selector so the simulation remains fast and interpretable.

## Slide 31
30 | CIRCUIT + EM CO-SIMULATION
Step 7: co-simulate the EM selector with the RF component
CLOSE THE MODEL
RF
COMPONENT
EM S2P
selector block
NEXT / TEST
PORT
Replace the ideal branch in the circuit schematic with the EM-generated multiport data.
Run State A and State B with the same RF component and port definitions.
Compare circuit-only, EM-only, and co-simulated results to isolate where the loss or mismatch comes from.
Save the exact EM project, mesh settings, stack-up, and exported file used for the thesis plot.
If the measured board disagrees, first check stack-up and reference planes before changing the topology.

## Slide 32
31 | KICAD LAYOUT
Step 8: transfer the validated dimensions into KiCad deliberately
PCB IMPLEMENTATION
1
Create the project
Set units, grid, net classes, board outline, and revision-controlled project folder.
2
Enter the stack-up
Use the manufacturer stack-up, dielectric thickness, Dk, copper thickness, and impedance rules.
3
Place footprints
Place RF component, link footprints, test connector, and nearby ground vias first.
4
Route RF
Use the AWR width and length as starting values; keep branch short and reference plane continuous.
5
Add fabrication details
Silkscreen population labels, DNP notes, polarity, connector direction, and test points.
6
Run checks
DRC, courtyard, annular ring, soldermask, fab drawing, and impedance review.
Do not assume AWR and KiCad use identical origin, layer naming, or pad geometry. Compare the actual copper dimensions after layout.

## Slide 33
32 | KICAD REVIEW CHECKLIST
Step 9: perform a layout review before fabrication
PRE-FAB
Geometry
Are W, Lbranch, pad dimensions, and connector launch close to the AWR model?
Ground
Is the reference plane continuous under the RF path? Are ground vias close enough to the transition?
Assembly
Can J_DIRECT and J_TEST be reworked without damaging the RF trace? Are DNP states unambiguous?
Mechanical
Can the test cable mate without bending the board or touching sensitive parts?
Documentation
Are stack-up, footprints, link values, DNP notes, and revision recorded?
Export a PDF of the final layout and annotate the RF current path. This is useful in the thesis and catches accidental detours.

## Slide 34
33 | MEASUREMENT CLOSURE
Step 10: validate the fabricated board and update the model
MODEL VS HARDWARE
AWR prediction
S11 / S21 / isolation plots with model version
KiCad release
Gerbers, drill files, stack-up, BOM, population state
Board measurement
Calibration, photographs, exact cable routing, raw Touchstone files
Correlation
Overlay measured and simulated traces; explain differences
Thesis result
Final path choice, error budget, limitations, and next revision
The goal is not a perfect first simulation. The goal is a traceable loop from assumptions to geometry to measurement.

## Slide 35
34 | EXECUTION PLAN
A manageable thesis schedule is: model, simulate, layout, measure, explain
PROJECT PLAN
Week 1
Requirements + stack-up
Confirm frequency span, manufacturer capability, connector, RF component, and measurement equipment.
Week 2
AWR schematic
Build ideal and transmission-line models; define State A and State B.
Week 3
AWR EM
Model branch, pads, vias, connector launch; run sensitivity sweep.
Week 4
KiCad layout
Implement the selected dimensions, add DNP notes, review and release fab files.
Week 5
Board measurement
Calibrate VNA, characterize State B, then rework to State A and repeat.
Week 6
Correlation + thesis
Overlay plots, explain mismatch, document rework and final recommendation.
Recommended first action: obtain the PCB stack-up and the RF component S-parameter file, then build the ideal State A / State B schematic in AWR.